List of modifications on the Existing standard Probe card (series number E128-RCT 50 ohm) from Circuit probe engineering

- The new probe card will have dimension as shown on layout.

- One 50 pins and one 34 pins 3M connectors with pin 1 position as shown on schematic will replace the 128 pins edge connector.

- Differential pair signals will be layout in parallel and on the same trace layer.

- All inductors will be located close to the connectors.

- All the decoupling capacitors will be located as close as possible to the probe pins.

- All resistors will be located around 1” from the probe pins solder pads.

- The 50 pin connector will be position on the center of the probe card as shown.

- The probe card will have 6 layers (50 ohm matched impedance ,full body gold ) in the following order:

  - Top traces layer.

  - Vdd layer.

  - Digital and Analog layer spit plane layer.( this plane will have jumpers located along the split line to allow for connect the 2 half planes  together )

  - Analog ground layer ( this plane will connect to the analog half plane )

  - Vcc layer.

  - Bottom traces layer.

- Unused traces will be connected direct to Digital or analog ground.